### PART 1 – GENERAL

  - SUMMARY

- This section includes the following:

- Chairs (Cafe™)

  - QUALITY ASSURANCE

- Installer Qualifications: An experienced installer who has completed installation of similar furnishings.

- Manufacturer Qualifications: Graber Manufacturing, Inc. is a skilled manufacturer of site furnishings since 1989.

- Source Limitations: For consistent quality in appearance and physical properties obtain each product from Graber Manufacturing, Inc.

- Product Options: Drawings indicate size, shape and dimensional requirements of furnishings for the purpose of customer sourcing.

  - SUBMITTALS

- Product Data: Include physical characteristics such as materials, specifications and finish.

- Drawings: Show details including dimensions, materials, and options for each product.

- Samples for Verification: Finish samples of the color and type of powder coat will be provided upon request.

- Maintenance Data: For each product include the recommended methods for repairing damage to the powder coat and materials finish will be provided.

  - DELIVERY, STORAGE AND HANDLING

- Store product(s) in original undamaged packaging and containers until ready for installation.

- Handle powder coated product(s) with sufficient care to prevent any scratches or damage to the finish.

  - WARRANTY

A. 	Site furnishings carry a five year manufacturer’s limited warranty against defects in materials and workmanship. The warranty period begins the date of invoice.

### PART 2 - PRODUCTS

  - ACCEPTABLE MANUFACTURERS

A.	Thomas Steele, a division of Graber Manufacturing, Inc. 1080 Uniek Drive, Waunakee, WI 53597. Toll free phone: 800-448-7931. Local phone: 608-849-1080.

  - MATERIALS

- e-Steele™ Shot Blast / E-Coat Primer / TGIC Powder Coating:

- The site furnishing steel shall be completely shot blasted to white metal with cast iron media.  Furnishings shall be treated with zinc phosphate and primed with an e-coat epoxy primer in an environmentally friendly closed loop 18 stage finishing process. Furnishings shall be cleaned with detergent and powder coated with super durable triglycidyl isocyanurate (TGIC) polyester powder.  The coatings thickness shall not be greater than 6 mils to ensure a durable finish that resists corrosion, chipping, abrasion, cracking and UV damage. (The use of silicone caulk for gap filling of joints shall not be allowed.)

- Color as selected by architect from manufacturer’s full range of standard colors.

  - CHAIRS

- Cafe™: The chair shall be the CFC-__ (insert seat style and with or without arms). Manufactured by Thomas Steele, a division of Graber Manufacturing, Inc.

  - Seat Frame:

    - Frame shall be constructed of 1” (25.4mm) diameter carbon steel tubing.

  - Seating Materials:

  - Perforated Metal:

        - Seat shall be constructed of 14 gauge (.075” (1.9mm)) thickness perforated carbon steel sheet with 3/8” (9.6mm) square holes place on 9/16” (14.3mm) centers.

        - Seat support members shall be constructed of 1/4” x 3” (6.4mm x 76.2mm) carbon steel flat bar; and 7/8” (22.3mm) diameter carbon steel tubing.

  - Wire Mesh:

        - Seat shall be constructed of .192” and .125” diameter Bright Wire.

        - Seat support members shall be constructed of ¼” x 3” (6.4mm x 76.2mm) carbon steel flat bar; and 7/8” (22.3mm) diameter carbon steel tubing.

- Terrace™: The chair shall be the TEC. Manufactured by Thomas Steele, a division of Graber Manufacturing, Inc.

  - Seating Materials:

    - Seat shall be constructed of 7/16” (11.2mm) diameter carbon rod; and 11 gauge (.1196” (3.1mm)) thickness carbon steel sheet.

- Fresco™: The chair shall be the FRC. Manufactured by Thomas Steele, a division of Graber Manufacturing, Inc.

  - Seating Materials:

    - Seat shall be constructed of 7/16” (11.2mm) diameter carbon rod; 5/16” (7.9mm) diameter carbon rod; and 11 gauge (.1196” (3.1mm)) thickness carbon steel sheet.

  - REFERENCES

- Flat Bar

- ASTM A36 Carbon Structural Steel

## Round Bar

## ASTM A36 Carbon Structural Steel

- Tubing:

    - ASTM A513 Electric-Resistance-Welded Carbon and Alloy Steel Mechanical Tubing

PART 3 – EXECUTION

  - INSTALLATION

- Install in accordance with manufacturer’s instructions.

- Embedded mounting: Material is to be extended a minimum of 10” (254mm) below finish surface and cast in concrete.

- Surface mounting: Location and drilling of holes for inserts included.

- Some assembly required.