### PART 1 – GENERAL

  - SUMMARY

- This section includes the following:

- Tables (Carnival™ Courtyard, Carnival™ Square, Carnival™ Curved, Carnival™ Picnic)

  - QUALITY ASSURANCE

- Installer Qualifications: An experienced installer who has completed installation of similar furnishings.

- Manufacturer Qualifications: Graber Manufacturing, Inc. is a skilled manufacturer of site furnishings since 1989.

- Source Limitations: For consistent quality in appearance and physical properties obtain each product from Graber Manufacturing, Inc.

- Product Options: Drawings indicate size, shape and dimensional requirements of furnishings for the purpose of customer sourcing.

  - SUBMITTALS

- Product Data: Include physical characteristics such as materials, specifications and finish.

- Drawings: Show details including dimensions, materials, and options for each product.

- Samples for Verification: Finish samples of the color and type of powder coat will be provided upon request.

- Maintenance Data: For each product include the recommended methods for repairing damage to the powder coat and materials finish will be provided.

  - DELIVERY, STORAGE AND HANDLING

- Store product(s) in original undamaged packaging and containers until ready for installation.

- Handle powder coated product(s) with sufficient care to prevent any scratches or damage to the finish.

  - WARRANTY

A. 	Site furnishings carry a five year manufacturer’s limited warranty against defects in materials and workmanship. The warranty period begins the date of invoice.

### PART 2 - PRODUCTS

  - ACCEPTABLE MANUFACTURERS

A.	Thomas Steele, a division of Graber Manufacturing, Inc. 1080 Uniek Drive, Waunakee, WI 53597. Toll free phone: 800-448-7931. Local phone: 608-849-1080.

  - MATERIALS

- e-Steele™ Shot Blast / E-Coat Primer / TGIC Powder Coating:

- The site furnishing steel shall be completely shot blasted to white metal with cast iron media.  Furnishings shall be treated with zinc phosphate and primed with an e-coat epoxy primer in an environmentally friendly closed loop 18 stage finishing process. Furnishings shall be cleaned with detergent and powder coated with super durable triglycidyl isocyanurate (TGIC) polyester powder.  The coatings thickness shall not be greater than 6 mils to ensure a durable finish that resists corrosion, chipping, abrasion, cracking and UV damage. (The use of silicone caulk for gap filling of joints shall not be allowed.)

- Color as selected by architect from manufacturer’s full range of standard colors.

  - TABLES

- Carnival™ Courtyard: The courtyard table shall be the CRT-__-__ (insert seat number and type (backed or flat), and top type) or the bar height table shall be the CRTB-__-__ (insert seat number and type (backed or flat), and top type). Manufactured by Thomas Steele, a division of Graber Manufacturing, Inc.

  - Table Frame:

    - Legs shall be constructed of 2 3/8” (60.4mm) diameter carbon steel tubing; bar height legs are 1 ½” (12.7mm x 76.2mm) square carbon steel tubing; 2” (50.8mm) square carbon steel tubing; and ¼” x 2 ½” (6.4mm x 63.5mm) carbon steel flat bar.

  - Table Top:

          - Round top shall be shall be constructed of a 42” diameter 11 ga. spun metal with a 1 ½” reinforced rolled ‘C’ lip.

          - Square top shall be constructed of 42” square 11 ga. spun metal with a 1 ½” reinforced rolled ‘C’ lip.

          - IPE wood shall be 1” x 3” (25.4mm x 76.2mm) nominal unfinished solid stock with eased edges.

          - Recycled plastic shall be 1” x 3” (25.4mm x 76.2mm) nominal derived from post-consumer waste and 100% high density polyethylene. Material shall be treated with a UV-inhibitor

  - Seating Materials:

        - Straps shall be constructed of ¼” x 1 ½” (6.4mm x 38.1mm) carbon steel flat bar.

        - Cross tubes shall be constructed of 1 5/8” (41.3mm) diameter carbon steel tubing.

        - Seat Support members shall be constructed of ¼” x 3” (6.4mm x 76.2mm) carbon steel flat bar; 5/8” (15.9mm) diameter carbon steel round bar; and ½” x 1 ½” (12.7mm x 38.1mm) carbon steel flat bar.

- Carnival™ Square: The 3 foot table shall be the CRT3-__-__ or the 4 foot table shall be the CRT4-__-__ (insert number of seats, and mounting option). Manufactured by Thomas Steele, a division of Graber Manufacturing, Inc.

  - Table Frame:

- Frame shall be constructed of 3/8” (9.6mm) carbon steel flat plate; 4” (101.6mm) square carbon steel tubing; and 2 ½” (63.5mm) square carbon steel tubing.

  - Table Top:

    - Top shall be constructed of ¼” x 1 ½” (6.4mm x 38.1mm) carbon steel flat bar; 1 5/8” (41.3mm) diameter carbon steel tubing; 2” (50.8mm) carbon steel angle; and ¼” x 1” (6.4mm x 25.4mm) carbon steel flat bar.

  - Seating Materials:

    - Pedestal seats shall be constructed of 2 3/8” (60.4mm) diameter carbon steel tubing; 3/8” x 3” (9.6mm x 76.2mm) carbon steel flat bar; ½” x 3” (12.7mm x 76.2mm) carbon steel flat bar; 1 5/8” (41.3mm) diameter carbon steel tubing; and ¼” x 1 ½” (6.4mm x 38.1mm) carbon steel flat bar.

    - Post mount seats shall be constructed of 3” (76.2mm) square carbon steel tubing; ½” x 3” (12.7mm x 76.2mm) carbon steel flat bar; 2” x 3” (50.8mm x 76.2mm) carbon steel angle; 1 5/8” (41.3mm) diameter carbon steel tubing; and ¼” x 1 ½” (6.4mm x 38.1mm) carbon steel flat bar.

- Carnival™ Curved: The table shall be the CRTC-__-__ (insert number of seats, and top style). Manufactured by Thomas Steele, a division of Graber Manufacturing, Inc.

  - Table Frame:

    - Legs shall be constructed of 1 ½” (12.7mm x 76.2mm) square carbon steel tubing; 2” (50.8mm) square carbon steel tubing; and ¼” x 2 ½” (6.4mm x 63.5mm) carbon steel flat bar.

  - Table Top:

    - Round top shall be shall be constructed of a 36” diameter 11 ga. spun metal with a 1 ½” reinforced rolled ‘C’ lip.

  - Seat Materials:

    - Seats shall be shall be constructed of 3/8” x 1 ½” (9.6mm x 38.1mm) carbon steel flat bar; ¼” x 1 ½” (6.4mm x 38.1mm) carbon steel flat bar.

- Carnival™ Picnic: The table shall be the CRTP-__-__ (insert size of table and whether it’s a set, and mounting style). Manufactured by Thomas Steele, a division of Graber Manufacturing, Inc.

  - Frame:

    - Table frame shall be constructed of ½” x 3” (12.7mm x 76.2mm) carbon steel flat bar; 2 3/8” (60.4mm) diameter carbon steel tubing.

    - Freestanding frame shall be constructed of 3” (76.2mm) carbon steel channel; 2 3/8” (60.4mm) diameter carbon steel tubing;  ½” x 3” (12.7mm x 76.2mm) carbon steel flat bar; and 3/8” x 3” (9.6mm x 76.2mm) carbon steel flat bar.

  - Top:

    - Table top shall be constructed of ½” x 3” (12.7mm x 76.2mm) carbon steel flat bar; 1 5/8” (41.3mm) diameter carbon steel tubing; and ¼” x 1 ½” (6.4mm x 38.1mm) carbon steel flat bar.

  - REFERENCES

- Flat Bar

- ASTM A36 Carbon Structural Steel

## Round Bar

## ASTM A36 Carbon Structural Steel

- Tubing

  - ASTM A513 Electric-Resistance-Welded Carbon and Alloy Steel Mechanical Tubing

- Stainless Steel

  - ASTM A312 Standard Specification for Seamless, Welded, and Heavily Cold Worked Austenitic Stainless Steel Pipes

PART 3 – EXECUTION

  - INSTALLATION

- Install in accordance with manufacturer’s instructions.

- Embedded mounting: Material is to be extended a minimum of 10” (254mm) below finish surface and cast in concrete.

- Surface mounting: Location and drilling of holes for inserts included.

- Some assembly required.