### PART 1 – GENERAL

  - SUMMARY

- This section includes the following:

- Genova Ash Receptacles (GNAR)

  - QUALITY ASSURANCE

A.	Installer Qualifications: An experienced installer who has completed installation of ash receptacles similar in material, design, and extent to that indicated for this project and whose work has resulted in construction with a record of successful in-service performance.

B.	Manufacturer Qualifications: A firm experienced in manufacturing ash receptacles similar to those required for this project.

- Source Limitations: Obtain each color, finish, shape and type of ash receptacles from a single source with resources to provide components of consistent quality in appearance and physical properties.

- Product Options: Drawings indicate size, shape and dimensional requirements of ash receptacles and are based on the specific system indicated.

  - REFERENCES

- Ash Receptacle Frame:

- Tubing

a. ASTM A500 Carbon Structural Steel

- Flat Bar

a. ASTM A36 Carbon Structural Steel

  - SUBMITTALS

- Product Data: Include physical characteristics such as shape, dimensions and finish for each ash receptacle.

- Shop Drawings: Show installation details for each ash receptacle.

C.	Samples for Verification: For the following ash receptacles, showing; (1) the color of the powder coat finish. Prepare 2 inch by 3.5-inch (50.8 mm by 87.5mm) powder coat samples (or larger) from the same material to be used to finish the product, (2) Stainless steel. Submit a sample piece for review.

D.       Maintenance Data: For each ash receptacle.

- Include recommended methods for repairing damage to the powder coat finish.

  - DELIVERY, STORAGE, AND HANDLING

- Store ash receptacle/s in original undamaged packaging and containers until ready for installation.

B.       Handle powder coated ash receptacle/s with sufficient care to prevent any scratches or damage to the finish.

  - WARRANTY

- Site furnishings are to carry a five year manufacturer’s limited warranty against defects in materials and workmanship. The warranty period begins the date the product is shipped from the manufacturer.

### PART 2 – PRODUCTS

### 2.1	ACCEPTABLE MANUFACTURERS

A.	Provide ash receptacle/s manufactured by the Thomas Steele division of Graber Manufacturing, Inc.

2.2	MATERIALS

A.	e-Steele™ E-Coat Epoxy / Powder Coating:

1.  The site furnishing shall receive an 18 stage finishing process to insure an extremely durable finish to resist corrosion, chipping, abrasion, cracking and UVA damage. The steel substrate shall be mechanically and chemically etched to insure proper finish adhesion, followed by a zinc phosphate bath for corrosion resistance. The site furnishing shall then be primed by immersion into a non-chrome seal rinse to enhance and supplement the corrosion resistance. The site furnishing shall then be immersed into an environmentally friendly e-coat epoxy liquid bath to insure that all surfaces, joints and crevices are covered. (The use of silicone caulk for gap filling of joints shall not be allowed.) The site furnishing shall be powder coated after complete fabrication with triglycidyl isocyanurate (TGIC) powder, a polyester coating that is electrostatically applied and baked at 400 degrees for 20 minutes. Powder coat shall not exceed thickness greater than (6 mils).

2.   Color as selected by architect from manufacturer’s full range of standard colors.

###### 2.3	ASH RECEPTACLES

A.	The ash receptacle shall be the GNAR as manufactured by Thomas Steele, a division of Graber Manufacturing, Inc.

- Frame Materials:

  - Rim shall be 5/8” (15.9mm) diameter carbon structural steel round bar.

Horizontal rings and cross braces shall be 1/4” x 2” (6.4mm x 50.8mm) carbon steel flat bar. Anchor plate shall be ½ x 3” x flat bar.

- Siding Material:

  - Vertical Steel Rod shall be 5/8” (15.9mm) diameter carbon structural steel round bar. Rod supports shall be 1/4” x 2” (6.4mm x 50.8mm) carbon structural steel flat bar.

- Fasteners:

  - All assembly fasteners shall be stainless steel.

PART 3 – EXECUTION

3.1       INSTALLATION

- Handle and install ash receptacles in accordance with manufacturer’s recommendations and installation instructions.

- Set ash receptacles secured to construction, level and true to line, in correct relationship to adjacent materials.