### PART 1 – GENERAL

  - SUMMARY

- This section includes the following:

- Trash Receptacles (Gramercy™)

  - QUALITY ASSURANCE

- Installer Qualifications: An experienced installer who has completed installation of similar furnishings.

- Manufacturer Qualifications: Graber Manufacturing, Inc. is a skilled manufacturer of site furnishings since 1989.

- Source Limitations: For consistent quality in appearance and physical properties obtain each product from Graber Manufacturing, Inc.

- Product Options: Drawings indicate size, shape and dimensional requirements of furnishings for the purpose of customer sourcing.

  - SUBMITTALS

- Product Data: Include physical characteristics such as materials, specifications and finish.

- Drawings: Show details including dimensions, materials, and options for each product.

- Samples for Verification: Finish samples of the color and type of powder coat will be provided upon request.

- Maintenance Data: For each product include the recommended methods for repairing damage to the powder coat and materials finish will be provided.

  - DELIVERY, STORAGE AND HANDLING

- Store product(s) in original undamaged packaging and containers until ready for installation.

- Handle powder coated product(s) with sufficient care to prevent any scratches or damage to the finish.

  - WARRANTY

A. 	Site furnishings carry a five year manufacturer’s limited warranty against defects in materials and workmanship. The warranty period begins the date of invoice.

### PART 2 - PRODUCTS

  - ACCEPTABLE MANUFACTURERS

A.	Thomas Steele, a division of Graber Manufacturing, Inc. 1080 Uniek Drive, Waunakee, WI 53597. Toll free phone: 800-448-7931. Local phone: 608-849-1080.

  - MATERIALS

- e-Steele™ Shot Blast / E-Coat Primer / TGIC Powder Coating:

- The site furnishing steel shall be completely shot blasted to white metal with cast iron media.  Furnishings shall be treated with zinc phosphate and primed with an e-coat epoxy primer in an environmentally friendly closed loop 18 stage finishing process. Furnishings shall be cleaned with detergent and powder coated with super durable triglycidyl isocyanurate (TGIC) polyester powder.  The coatings thickness shall not be greater than 6 mils to ensure a durable finish that resists corrosion, chipping, abrasion, cracking and UV damage. (The use of silicone caulk for gap filling of joints shall not be allowed.)

- Color as selected by architect from manufacturer’s full range of standard colors.

  - TRASH RECEPTACLES

- Gramercy™: The receptacle shall be the GRTR-__ (insert gallon size and side type). Manufactured by Thomas Steele, a division of Graber Manufacturing, Inc.

  - Frame Materials:

    - Horizontal rings shall be constructed of 3/8” x 2” (9.6mm x 50.8mm) carbon steel flat bar.

    - Rosette ring shall be constructed of 3/16” x 1” (4.8mm x 25.4mm) carbon steel flat bar.

    - Wood ring shall be constructed of ¼” x 2” (6.4mm x 50.8mm) carbon steel flat bar.

    - Base shall be constructed of 3/16” (4.8mm) carbon steel plate.

  - Siding Materials:

  - Vertical straps shall be constructed of ¼” x 2” (6.4mm x 50.8mm) carbon steel flat bar.

  - Decorative rings shall be constructed of ½” (12.7mm) diameter carbon steel rod. Rosettes shall be constructed of ¼” (6.4mm) thick cast iron.

  - IPE wood shall be 1” x 3” (25.4mm x 76.2mm) nominal unfinished solid stock with eased edges.

  - Recycled plastic shall be 1” x 3” (25.4mm x 76.2mm) nominal derived from post-consumer waste and 100% high density polyethylene. Material shall be treated with a UV-inhibitor.

  - REFERENCES

- Flat Bar

- ASTM A36 Carbon Structural Steel

PART 3 – EXECUTION

  - INSTALLATION

- Install in accordance with manufacturer’s instructions.

- Embedded mounting: Material is to be extended a minimum of 10” (254mm) below finish surface and cast in concrete.

- Surface mounting: Location and drilling of holes for inserts included.

- Some assembly required.